## Slide 1: Proposal of C-Lang Intelligent Function Unit for Azure IoT
Sr. IoT Cloud Solution Architect
Hisashi Goto
Version 0.3
Nov 8th 2021

## Slide 2: Drafting Proposal of Demo System
C言語インテリ機能ユニットを実行させる対象装置を、IoT Plug and Playのに対応したデバイスモデルを作成し、クラウド上からリモートで操作する
iQ-R Plug&Play Device Model
Debian9 Stretch
CITL_read
CITL_Write
Sample Image
Plug&Play Azure SaaS Service

## Slide 3: Ref: About Azure IoT SDK for Python
python --version
wget https://www.python.org/ftp/python/3.7.10/Python-3.7.10.tgz
tar zxvf Python-3.7.10.tgz
cd Python-3.7.10/
./configure --enable-optimizations
make -j4
sudo make altinstall
pip install azure-iot-device
install python package for Azure IoT
Make it sure Python version == 3.7?
How to install Python 3.7
git clone https://github.com/Azure/azure-iot-sdk-python
Clone Sample Codes
Change Directory to PnP Sample code
cd azure-iot-sdk-python\azure-iot-device\samples\pnp

## Slide 4: Azure.iot.device Package & Classes
https://docs.microsoft.com/en-us/python/api/azure-iot-device/azure.iot.device?view=azure-python
azure.iot.device.aio
 Azure IoT Device Library - Asynchronous
IoTHubDeviceClient
IoTHubModuleClient
ProvisioningDeviceClient
azure.iot.device
 Azure IoT Device Library - Synchronous
Message Represents a message to or from IoTHub
MethodRequest Represents a request to invoke a direct method.
MethodResponse Represents a response to a direct method.
Registration using Device provisioning Service

## Slide 5: Device Model
deviceInformation
+swVersion (string) = “Kernel 4.9.76-rt61-ltsi”
+manufacturer (string) = “MELCO”
+model(string) = “RD55UP12-V”
+osName(string) = “debian” or “linux”
+processorArchitecture(string) = “arm9”
+processorManufacturer=“xxxx”
+totalStorage(int) = 8192 (8GB)
+totalMemory(int) = 1024
RD55UP12-V
Property (deviceTwin)
Command
CITL_ToBuf
CITL_FromBuf
CITL_GetErrInfo
CITL_GetLEDStatus
CITL_SetLEDtStatus
mdrRecieve
mdrSend
mdrTypeRead
mdrGetLabelInfo
Telemetry (TBD)
xxxxx ( CITL_StartCollectData関数を使用してスキャンしたデータ
アドバイス募集

## Slide 6: Skelton of Digital Twin Model 1/3
C:\Temp\adtMELCOsequenser
Folder:

## Slide 7: Skelton of Digital Twin Model 2/3

## Slide 8: Skelton of Digital Twin Model 3/3
Device Information is Pre Defined by Microsoft

## Slide 9: Plug and Play Development on Device side
https://docs.microsoft.com/en-us/azure/iot-develop/concepts-developer-guide-device?pivots=programming-language-python

## Slide 10: Python Pseudo Code -- Main
Ref code simple_thermostat.py

## Slide 11: Python Pseudo Code – Helper Module

## Slide 12: Python Pseudo Code – Model ID
device_client = IoTHubDeviceClient.create_from_symmetric_key(
symmetric_key=symmetric_key,
hostname=registration_result.registration_state.assigned_hub,
device_id=registration_result.registration_state.device_id,
product_info=model_id,
)
Note
Use IoTHubModuleClient for IoT Edge module
Tell Model ID Payload If you use DPS at provisioning stage
{
"modelId" : "dtmi:com:example:Thermostat;1"
}
Example of JSON payload for DPS

## Slide 13: Python Pseudo Code -- Commands
W.I.P.

## Slide 14: Defender for IoT

## Slide 15: Defender for IoT – Install microAgent
curl https://packages.microsoft.com/config/debian/stretch/multiarch/prod.list > ./microsoft-prod.list
sudo cp ./microsoft-prod.list /etc/apt/sources.list.d/
curl https://packages.microsoft.com/keys/microsoft.asc | gpg --dearmor > microsoft.gpg
sudo cp ./microsoft.gpg /etc/apt/trusted.gpg.d/
sudo apt-get install defender-iot-micro-agent
How to Install

## Slide 16: Defender for IoT – Register microAgent to IoT Hub
RD55UP12-V
Register microAgent to IoT Hub

## Slide 17: Set Security Information to Device

## Slide 18: Python Pseudo code -- Send Telemetry
async def send_telemetry_from_temp_controller(device_client, telemetry_msg, component_name=None):
msg = Message(json.dumps(telemetry_msg))
msg.content_encoding = "utf-8"
msg.content_type = "application/json"
if component_name:
msg.custom_properties["$.sub"] = component_name
await device_client.send_message(msg)
}
See Component Name if you use nested components

## Slide 19: Pseudo Python Code – Properties (read only)
await device_client.patch_twin_reported_properties({"maxTempSinceLastReboot": 38.7})
Report Properties of flat model
{
"reported": {
"maxTempSinceLastReboot" : 38.7
}
}
This method generates Device-Twin Json to update property
inner_dict = {}
inner_dict["targetTemperature"] = 38.7
inner_dict["__t"] = "c"
prop_dict = {}
prop_dict["thermostat1"] = inner_dict
await device_client.patch_twin_reported_properties(prop_dict)
Report properties of a Component using inner dictionary
{
"reported": {
"thermostat1" : {
"__t" : "c",
"maxTempSinceLastReboot" : 38.7
}
}
}
 {} Inner dictionary

## Slide 20: Pseudo Python Code – Properties (writable)
prop_dict = {}
prop_dict["targetTemperature"] = {
"ac": 200,
"ad": "reported default value",
"av": 0,
"value": 23.2
}
await device_client.patch_twin_reported_properties(prop_dict)
Report to writable property, it must include the ack values defined in the conventions.
{
"reported": {
"targetTemperature": {
"value": 23.2,
"ac": 200,
"av": 0,
"ad": "reported default value"
}
}
}
 ack version

## Slide 21: Python Pseudo Code – Properties (subscribe)
async def execute_property_listener(device_client):
ignore_keys = ["__t", "$version"]
while True:
patch = await device_client.receive_twin_desired_properties_patch()
version = patch["$version"]
prop_dict = {}
for prop_name, prop_value in patch.items():
if prop_name in ignore_keys:
continue
else:
prop_dict[prop_name] = {
"ac": 200,
"ad": "Successfully executed patch",
"av": version,
"value": prop_value,
}
await device_client.patch_twin_reported_properties(prop_dict)
Blocking call
{
"desired" : {
"targetTemperature": 23.2,
"$version" : 3
},
"reported": {
"targetTemperature": {
"value": 23.2,
"ac": 200,
"av": 3,
"ad": "complete"
}
}
}
Must includes ack in Reported message
 Get version info from Desired Properties

## Slide 22: Python Pseudo Code – Commands
command_request = await device_client.receive_method_request("thermostat1*reboot")
[Component Name] * [ Command Name]
def create_max_min_report_response(values):
response_dict = {
"maxTemp": max_temp,
"minTemp": min_temp,
"avgTemp": sum(avg_temp_list) / moving_window_size,
"startTime": (datetime.now() - timedelta(0, moving_window_size * 8)).isoformat(),
"endTime": datetime.now().isoformat(),
}
response_payload = json.dumps(response_dict, default=lambda o: o.__dict__, sort_keys=True)
return response_payload
Wait for Direct Method from IoT Service
Respond to IoT Service
Serialize response to JSON document
command_response = MethodResponse.create_from_method_request(
command_request, response_status, response_payload
)
try:
await device_client.send_method_response(command_response)
except Exception
print(“xxxxxxxxx”)

## Slide 24: Digital Twin – Demo? (2nd phase)

## Slide 25: Network Setting
ip link set dev eth0 up
Boot Debiun9 on RD55UP12
ip addr show
 Check if eth0 is down ( mtu 1500 qdisc noop state DOWN group default qlen 1000)
ip addr show
 Check if eth0 is UP and check IP address is assigned from DHCP (ex 192.168.1.10/24)
sudo nano /etc/network/interfaces
allow-hotplug eth0
iface eth0 inet static
address 192.168.1.10
netmask 255.255.255.0
gateway 192.168.1.1
allow-hotplug eth1
iface eth1 inet static
address 192.168.1.3
netmask 255.255.255.0
gateway 192.168.3.1
Insert new lines
sync
poweroff
Reboot RD55UP12
Save & Exit editor
Shutdown RDP55UP12
route add default gw 192.168.1.1
ping yahoo.com
ssh login
ssh admin@192.168.3.3
password : password

## Slide 26: Debian setting – apt-get package
nano /etc/apt/source.list
Open a file
deb http://ftp.de.debian.org/debian stretch main
Edit or Replace “http://xxxxxxx”
Save and Exit Editor
Update Debian packages
apt-get update
apt-get install –y autoconf libtool automake build-essential gdb
apt-get install –y apt-transport-https
apt-get install -y build-essential tk-dev libncurses5-dev libncursesw5-dev libreadline6-dev libdb5.3-dev libgdbm-dev libsqlite3-dev libssl-dev libbz2-dev libexpat1-dev liblzma-dev zlib1g-dev libffi-dev
apt-get update
Python dependencies

## Slide 27: Python Install
mkdir python37
cd python37
wget https://www.python.org/ftp/python/3.7.0/Python-3.7.0.tgz --no-check-certificate
tar zxf Python-3.7.0.tgz
cd Python-3.7.0
./configure
make -j 4
 Up to 4 jobs in parallel
python3.7 -V
 Check version
ln -s /usr/local/bin/python3.7 /usr/local/bin/python3
python3 -V
 Check version
./configure --enable-optimizations
If you want build all stable optimizations active(PG0, etc)

## Slide 28: Install SIP package
https://src.fedoraproject.org/lookaside/pkgs/sip/
cd /mnt/c/temp/mitsubishiCITL/
tar –xzf sip-4.19.25.tar.gz
cd sip-4.19.25
python3 configure.py
Download SIP package from the link
make –j 4
make install
Build SIP package
Check if SIP was installed?
sip -V
Note: my working env: WSL Ubuntu20.04

## Slide 29: Shutdown MELIPC
sync
poweroff

## Slide 30: Date Time Setting
GX Work3
メニューバー(TOP) : オンライン
プルダウンメニュー： 時計設定
R08CPUの時刻が、RD55UP12-Vに同期されるので、
RD55UP12-V側で時刻設定を行うことができない。
R08CPU機器側で時刻設定を行わないと、
Python 3.7のコンパイルで問題が発生する

## Slide 31: Trouble Shooting : R08CPU – Error Code : H2200

## Slide 32: Azure IoT SDK for Python –API for Device Provisioning
https://docs.microsoft.com/ja-jp/python/api/azure-iot-device/azure.iot.device?view=azure-python
Create Provisioning Device Client
 Registration of a device with provisioning service using Symmetric Key or X509
create_from_symmetric_key(provisioning_host, registration_id, id_scope, symmetric_key, **kwargs)
create_from_x509_certificate(provisioning_host, registration_id, id_scope, x509, **kwargs)
global.azure-devices-provisioning.net
websockets (bool) : false(defalt)
cipher (str or list) : cipher suite strings
proxy_options : if necessary…
keepalive (int) : 60 sec(default)
(string) : copy and paste from DPS servcie
retister()
Register the device with the provisioning service
It Returns RegistrationResult(operation_id, status, registration_state=None)
X509 Class (optional pass-phrase)
Python Package : azure.iot.device.aio
Constructor: X509(cert_file, key_file, pass_phrase=None)
“1234” (next slide)
python-device.key.pem (next slide)
it is set by OS-ENV variable
from azure.iot.device import X509

## Slide 33: DPS example – step-by-step
https://docs.microsoft.com/ja-jp/azure/iot-dps/quick-create-simulated-device-x509?tabs=linux&pivots=programming-language-python
git clone https://github.com/Azure/azure-iot-sdk-python.git --recursive
Clone Sample Code
Check OpenSSL version
openssl version
 1.1.0 was installed in CITL
Install git
apt install git-all
openssl req -outform PEM -x509 -sha256 -newkey rsa:4096 -keyout ./python-device.key.pem -out ./python-device.pem -days 365 -extensions usr_cert -subj "/CN=Python-device-01"
Create self-signed X.509 device certificate
Enter PEM pass phrase: 1234
Verifying - Enter PEM pass phrase: 1234
Enter pass-pharse(1234) in command prompt
Confirm these 2 files are generated…
 Coffee break (wait for 10-15min)
DPS’s registration ID for the IoT device must match subject name on its device certificate. If you generated a self-signed test certificate, Python-device-01 is both the subject name and the registration ID for the device.
How to find out Subject Name in X.509 certificate
certutil python-device.pem
Output of the command
OS ENV variable : DPS_X509_REGISTRATION_ID

## Slide 34: DPS example – step-by-step
Azure Portal : Create IoT HUb

## Slide 35: DPS example – step-by-step
After it was created … Click Go to resource
Azure Portal  Create DPS Service

## Slide 36: DPS example – step-by-step
Copy them to MemoPad
Azure Portal  DSP Setting

## Slide 37: DPS example – step-by-step
Azure Portal  DPS Service
Select the python-device.pem
(OPTIONAL)
Update the Initial device twin state

## Slide 38: DPS example – step-by-step
Variable name | Description
PROVISIONING_HOST | This value is the global endpoint used for connecting to your DPS resource
PROVISIONING_IDSCOPE | This value is the ID Scope for your DPS resource
DPS_X509_REGISTRATION_ID | This value is the ID for your device. It must also match the subject name on the device certificate
X509_CERT_FILE | Your device certificate filename
X509_KEY_FILE | The private key filename for your device certificate
PASS_PHRASE | The pass phrase you used to encrypt the certificate and private key file (1234).
Edit Sample Code: (provisioning_x509.py)
cd azure-iot-sdk-python/azure-iot-device/samples/async-hub-scenarios
Set ENV variables ( EXPORT in bash ex.. export PROVISIONING_IDSCOPE=###### )
provisioning_x509.py (sample source code)
Import from azure.iot.device.aio

## Slide 39: Python Programing
/mnt/c/temp/pnp_python_demo/azure-iot-sdk-python/azure-iot-device/samples/pnp
Base Code Location
temp_controller_with_thermostats.py
VSCode Editor
 Insert : from azure.iot.device import X509
 Insert : from CITL.LinuxPy import *

## Slide 40: Python Programing
Modify provision_device (symmetric_key  x509)
Original
async def provision_device(provisioning_host, id_scope, registration_id, x509, model_id):
provisioning_device_client = ProvisioningDeviceClient.create_from_x509_certificate(
provisioning_host=provisioning_host,
registration_id=registration_id,
id_scope=id_scope,
x509=x509,
)
After

## Slide 41: Python Programing
Modify provision_device (symmetric_key  x509)
Original
After
id_scope = os.getenv("IOTHUB_DEVICE_DPS_ID_SCOPE")
registration_id = os.getenv("IOTHUB_DEVICE_DPS_DEVICE_ID")
x509 = X509(
cert_file=os.getenv("IOTHUB_DEVICE_X509_CERT"),
key_file=os.getenv("IOTHUB_DEVICE_X509_KEY"),
)
registration_result = await provision_device(
provisioning_host, id_scope, registration_id, x509, model_id
)

## Slide 42: Python Programing
Modify provision_device (symmetric_key  x509)
Original
device_client = IoTHubDeviceClient.create_from_x509_certificate(
x509=x509,
hostname=registration_result.registration_state.assigned_hub,
device_id=registration_result.registration_state.device_id,
product_info=model_id,
)
After

## Slide 43: Python Programing
Original
Original DTDL model
Thermostat
Controller
thermostat1
thermostat2
DTDL I/F: Thermostat
Device
Info
deviceInformation
model_id
Next Slide
Referenced Python Code…

## Slide 44: Modeling DTDLv2 – device information
Edit DTDLv2 model
Create Property (Device info)
Thermostat
Controller
Device
info
model_id
thermostat1
thermostat2
deviceInformation
 See Previous slide
+swVersion (string) = “Kernel 4.9.76-rt61-ltsi”
+manufacturer (string) = “MELCO”
+model(string) = “RD55UP12-V”
+osName(string) = “debian” or “linux”
+processorArchitecture(string) = “arm9”
+processorManufacturer=“xxxx”
+totalStorage(int) = 8192 (8GB)
+totalMemory(int) = 1024
RD55UP12-V
deviceInformation
Referenced Model

## Slide 45: Reference : Device Information Model
https://devicemodels.azure.com/dtmi/azure/devicemanagement/deviceinformation-1.json
{
"@context": "dtmi:dtdl:context;2",
"@id": "dtmi:azure:DeviceManagement:DeviceInformation;1",
"@type": "Interface",
"displayName": "Device Information",
"contents": [
{
"@type": "Property",
"name": "manufacturer",
"displayName": "Manufacturer",
"schema": "string",
"description": "Company name of the device manufacturer. This could be the same as the name of the original equipment manufacturer (OEM). Ex. Contoso."
},
{
"@type": "Property",
"name": "model",
"displayName": "Device model",
"schema": "string",
"description": "Device model name or ID. Ex. Surface Book 2."
},
{
"@type": "Property",
"name": "swVersion",
"displayName": "Software version",
"schema": "string",
"description": "Version of the software on your device. This could be the version of your firmware. Ex. 1.3.45"
},
{
"@type": "Property",
"name": "osName",
"displayName": "Operating system name",
"schema": "string", (Continue….)

## Slide 46: Modeling DTDLv2
Command
CITL_ToBuf(destAddr)
CITL_FromBuf(srcAddr)
iqrcntl
Controller
Device
info
model_id
rd55up12v
deviceInformation
Telemetry
temperature :
Edit DTDLv2 model
ToDo: from CITL_LinuxPy import *
 Used for Debugging
Continuous Read buf(addr=16384)
increment buf … then stop if buf >500
file:///C:/Users/higoto/OneDrive%20-%20Microsoft/CustomerInfomation/Mitsubishi/ClangIntelligentUnit/CITL_Linux_Manual/MELSEC_iQ-R_C_intelligent_function_module_Linux_Startup_manual-J.pdf
 Write(destAddr=16284)
 Read(srcAddr=16284)
Property
iqrcntlstatus(enum)
 Good or Bad
rd55up12v
iqrcntl
Telemetry
CITL_16384(integer)
Component
deviceInformation
rd55up12v
 dtmi:azure:DeviceManagement:DeviceInformation;1
 dtmi:com:example:rd55up12v;1
DTDL ID
(previous slide)

## Slide 47: FYI: How to Create DTDL Model using VS Code…
 example: rd55up12v
Create Plug-and-Play model for RD55UP12V
 Modify dtmi ID if you want

## Slide 48: Create DTDL Model – iqrconl
You need only these 2 components
Directory: C:\temp\mitsubihiCITL\r55up12v_DTDL
2 x Components are defined

## Slide 49: Create DTDL Model – rd55up12v
Directory: C:\temp\mitsubihiCITL\r55up12v_DTDL
2 x Direct Methods are defined

## Slide 50: Create DTDL Model – rd55up12v

## Slide 51: Coding DTDL model – rd55up12v
DTDL model: rd55up12v
Python – Sample Code

## Slide 52: Coding DTDL model – rd55up12v
DTDL model: rd55up12v
Python – Sample Code
request
response

## Slide 53: Coding DTDL modle – rd55up12v
Python – Sample Code
DTDL model: rd55up12v
request
response

## Slide 54: Coding DTDL model – iqrcontl
from enum import IntEnum
Import IntEnum
Property Name (see next slide)
Notes: IntEnum Class : you can compare enum to Integner value
For example : if (Status.Good == 0)

## Slide 55: Coding DTDL model – iqrcontl
DTDL model: iqrcontl
Property Name
Enum value (see previous slide)
Sample Code – Python

## Slide 56: Coding DTDL model – command listener
Main loop (python)
listeners = asyncio.gather(
execute_command_listener(
device_client,
method_name=“Hello",
user_command_handler=hello_handler,
create_user_response_handler=hello_resposne
),
execute_command_listener(
device_client,
rd55up12v_component_name,
method_name="CITL_ToBuf_Single",
user_command_handler=RD55UP12V.citl_tobuf_single_handler,
create_user_response_handler=RD55UP12V.citl_tobuf_single_response,
),
execute_command_listener(
device_client,
rd55up12v_component_name,
method_name="CITL_FromBuff_Single",
user_command_handler=RD55UP12V.citl_frombuf_single_handler,
create_user_response_handler=RD55UP12V.citl_from_buf_single_response,
),
execute_property_listener(device_client),
)
Method I/F of command_listener
Handler program for the command or direct method
(Optional) handler to create response payload
DTDL model (iqrcontl)
This property is deprecated. Either value, synchronous or asynchronous, has the same meaning

## Slide 57: Coding DTDL model – command listener
command_name: { Hello,
rd55up12v*CITL_ToBuf_Single,
rd55up12v*CITL_FromBuf_Single }
values = json payload of direct method
 Wait for Direct Method from IoT Hub
Handler program for the command or direct method
(Optional) handler to create response payload
--see next slide --

## Slide 58: FYI: Helper method – create_response_payload_with_status
def create_response_payload_with_status(command_request, method_name, create_user_response=None):
if method_name:
response_status = 200
else:
response_status = 404
if not create_user_response:
result = True if method_name else False
data = "executed " + method_name if method_name else "unknown method"
response_payload = {"result": result, "data": data}
else:
response_payload = create_user_response(command_request.payload)
return (response_status, response_payload)
You need implement of generating Response Payload
hello_response

## Slide 59: Coding DTDL model –handlers for Hello command

## Slide 60: Coding DTDL model – CITL_ToBuf_Single handlers

## Slide 61: Coding DTDL model – iqrcontl
DTDL model: iqrcontl

## Slide 62: Programming Guide

## Slide 63: Python Programming – Plug and Play models
Original Code : temp_controller_with_themostats.py
rd55up12v_digital_twin_model_identifier = “dtmi:com:example:rd55up12v;1”
model_id = “dtmi:com:example:iqrcntl;1”
 Do not change
rd55up12v_component_name = "rd55up12v"
02028527F1210241-E
 New code : iqr_controller_with_r55up12v.py
ex. RD55UP12V serial number
 Read Only property of rd55up12v

## Slide 64: Python Programming – Plug and Play models
properties_rd55up12v = pnp_helper.create_reported_properties(
rd55up12v_component_name, xxxxxx=######
}
properties_r55up12v

## Slide 65: Python Programming – Plug and Play models
global RD55UP12V
RD55UP12V = Rd55up12v(rd55up12v_component_name, 10)
rd55up12v_component_name
Delete
You need to define class
class Rd55up12v(object):
class Thermostat(object):
Refer to Python class Constructor __init__ ToDo : change arg…)
 CITL_ToBuf_Single

## Slide 66: Reference : pnp_helper.py
Python Helper module for Azure IoT
create_telemetry( telemetry_msg, component_name= xxx )
Take the raw telemetry message in the dictionary
return msg
create_reported_properties (component_name= xxx, **prop_kwargs)
Take in user properties passed as keyword argments (kwargs)
return prop_dict  pnp specific reported properties
deviceInformation or rd55pu12v or None
create_response_payload_with_status( command_request, method_name, create_user_response= yyy )
Create response for command request
return : response_status  200(ok), or 404(error)
response_payload  create_user_response_handler generates response of the command
Used for reading Static Property (read only)
(ex deviceInformation)

## Slide 67: Reference : pnp_helper.py
create_reported_properties_from_desired( patch )
Take patch(JSON) from device twin desired properties, then
Create device twin reported properties
return properties_dict
CLASS: PnPproperties
 Dictionary of properties
FYI:
_to_value_dict(self)
all_attr = list(( x for x in self.__dict__ )
inner = { key: { “value”: getattr(self, key) for key in all_attrs }
_to_simple_dict(self)
all_simple_attr = list(( x for x in self.__dict__ )
inner = { key: { “value”: getattr(self, key) for key in all_simple_attrs }
 Property listener use it

## Slide 68: Python Programming – Define Rd55up12v Class
Import CITL python package
Initialize CITL function

## Slide 69: Python Programing
export IOTHUB_DEVICE_X509_CERT=<full path to folder>sampleDevice01_cert.pem
export IOTHUB_DEVICE_X509_KEY=<full path to folder>sampleDevice01_key.pem
OS Environment for Python code (X509)

## Slide 70: Azure IoT Samples for Python
https://github.com/azure-samples/azure-iot-samples-python/tree/master/
Binder for Direct Methods
listeners = asyncio.gather(
execute_command_listener(
device_client,
method_name="reboot",
user_command_handler=reboot_handler,
create_user_response_handler=create_reboot_response,
),
execute_command_listener(
device_client,
method_name="getMaxMinReport",
user_command_handler=max_min_handler,
create_user_response_handler=create_max_min_report_response,
),
execute_property_listener(device_client),
)
 Bind to method “reboot”
 Method Handlers
def create_reboot_response(values):
response = {"result": True, "data": "reboot succeeded"}
return response
async def reboot_handler(values):
if values and type(values) == int:
print("Rebooting after delay of {delay} secs".format(delay=values))
asyncio.sleep(values)
print("maxTemp {}, minTemp {}".format(max_temp, min_temp))
print("Done rebooting")
async def execute_command_listener( device_client, method_name, user_command_handler, create_user_response_handler ):
while True: ……
async def execute_property_listener(device_client):
ignore_keys = ["__t", "$version"]
while True: ….
Listeners

## Slide 71: Plug & Play Sample
https://github.com/Azure/azure-iot-sdk-python/tree/master/azure-iot-device/samples/pnp
export IOTHUB_DEVICE_SECURITY_TYPE=“DPS”
export IOTHUB_DEVICE_DPS_ID_SCOPE=“<ID Scope of DPS instance>”
export IOTHUB_DEVICE_DPS_DEVICE_ID=“<Device’s ID>”
export IOTHUB_DEVICE_DPS_DEVICE_KEY=“<Device’s security key >”
export IOTHUB_DEVICE_DPS_ENDPOINT="global.azure-devices-provisioning.net"
ENVIRONMENT setting (bash)
 Python-device-01 (X.509)
 Not used it for X.509

## Slide 72: IoT Central Device Registration using X.509

## Slide 73: Connect devices with X.509 certificates -- Python
https://docs.microsoft.com/en-us/azure/iot-central/core/how-to-connect-devices-x509?pivots=programming-language-python
Prerequisites
Node.js version 6 or later
Azure IoT SDK for Node.js
 Needed for generating X.509 certificates (download)
https://github.com/Azure/azure-iot-sdk-node/archive/master.zip
 https://nodejs.org
IoT Central  Create Enrollment Group
 Type group name
Refresh Web Browser
Next 2 Slide later

## Slide 74: Connect devices with X.509 certificates -- Python
Generate X.509 Certificate (using Node.js )
Unzip master.zip to C:\temp\x509deviceCert
 download from
https://github.com/Azure/azure-iot-sdk-node/archive/master.zip
Using WSL of laptop {C
cd /mnt/c/temp\x509deviceCert
cd azure-iot-sdk-node/provisioning/tools
npm install
node create_test_cert.js root mytestrootcert
Create root certificate
node create_test_cert.js device sample-device-01 mytestrootcert
Create Device Certificate
Open WSL terminal
 /usr/bin/npm install
Filename created | contents
mytestrootcert_cert.pem | The public portion of the root X509 certificate
mytestrootcert_key.pem | The private key for the root X509 certificate
mytestrootcert_fullchain.pem | The entire keychain for the root X509 certificate.
sampleDevice01_cert.pem | The public portion of the device X509 certificate
sampleDevice01_key.pem | The private key for the device X509 certificate
sampleDevice01_fullchain.pem | The entire keychain for the device X509 certificate.
Use them IoT Central
(next 2 slide)
Uploaded file to …
git clone https://github.com/Azure/azure-iot-sdk-python.git

## Slide 75: Connect devices with X.509 certificates -- Python

## Slide 76: Connect devices with X.509 certificates -- Python
Select mytestrootcert_cert.pem from Local PC
Copy them to Memopad
Your Verification Code will be here 
Copy Verification Code
(Next Slide)
Notes: Primary
25904854F3723BFCF4A7B08AB3AC00A790AD1756
Subject
mytestrootcert
Thumprint
25904854F3723BFCF4A7B08AB3AC00A790AD1756
Verification Code (only 17 hours) 05B505B43C2C22736DEA1242611D00FBD1BCE8987801B1B1

## Slide 77: Connect devices with X.509 certificates -- Python
node create_test_cert.js verification --ca mytestrootcert_cert.pem --key mytestrootcert_key.pem --nonce {verification-code}
Run it on your laptop
certificate verification_cert.pem
This command will generate files:
Select the file
Copy Verification Code
run
Paste Verification Code
Click save button on 
top of your browser

## Slide 79: Setting IoT Central

## Slide 80: Import Models: IQ-R Control Device & RD55UP12-V

## Slide 81: Import Models: IQ-R Control Device & RD55UP12-V

## Slide 82: Import Models: IQ-R Control Device & RD55UP12-V

## Slide 83: Create a default view --

## Slide 84: Create a default view --

## Slide 85: Create A Dashboard

## Slide 87: Create a default view -- Overview

## Slide 88: Create a default view – About

## Slide 89: Azure IoTCentral SDK for Python
https://github.com/iot-for-all/iotc-python-client